## Slide 1: Planning and Navigation

## Slide 2: Competencies for Navigation
Navigation is composed of localization, mapping and motion planning
  Different forms of motion planning inside the cognition loop from R. Siegwart
"Position"
Global Map
Perception
Motion Control
Cognition
Real World
Environment
Localization
Path
Environment Model
Local Map

## Slide 3: Outline of this Lecture
Motion Planning
  State-space and obstacle representation
    Work space
    Configuration space
  Global motion planning
    Optimal control (not treated)
    Deterministic graph search
    Potential fields
    Probabilistic / random approaches
  Local collision avoidance
    BUG
    VFH
    ND
    ...

## Slide 4: The Planning Problem (1/2)
The problem: find a path in the work space (physical space) from the initial position to the goal position avoiding all collisions with the obstacles
Assumption: there exists a good enough map of the environment for navigation.
  Topological
  Metric
  Hybrid methods

## Slide 5: The Planning Problem (2/2)
We can generally distinguish between
  (global) path planning and
  (local) obstacle avoidance.
First step:
  Transformation of the map into a representation useful for planning
  This step is planner-dependent
Second step:
  Plan a path on the transformed map
Third step:
  Send motion commands to controller
  This step is planner-dependent (e.g. Model based feed forward, path following)

## Slide 6: Map Representations
Topological Map
(Continuous Coordinates)
Occupancy Grid Map
(Discrete Coordinates)
K-d Tree Map (Quadtree)
Large memory requirement of grid maps
> k-d tree recursively breaks the environment into k pieces
Here k = 4, quadtree

## Slide 7: Topological Map

## Slide 8: Topological Maps
Edges can carry weights
Standard Graph Theory Algorithms (Dijkstra's algorithm)
Good abstract representation
Several graphs for any world
Assumption: Robot can travel between nodes
Tradeoff in # of nodes:
complexity vs. accuracy
Limited information

## Slide 9: Grid World
Two dimensional array of values
Each cell represents a square of real world
Typically a few centimeters to a few dozen centimeters

## Slide 10: Alternative Representations
Waste lots of bits for big open spaces
KD-trees
x < 5
free
y<5
occupied
free

## Slide 11: QuadTree OctTree

## Slide 12: Work Space  Configuration Space
State or configuration q can be described with k values qi
What is the configuration space of a mobile robot?
Work Space
Configuration Space:
Planning in configuration space
the dimension of this
space is equal to the Degrees of Freedom (DoF)
of the robot
Example: manipulator robots

## Slide 13: Configuration Space for a Mobile Robot
Mobile robots operating on a flat ground have 3 DoF: (x, y, θ)
For simplification, in path planning mobile roboticists often assume that the robot is holonomic and that it is a point. In this way the configuration space is reduced to 2D (x,y)
Because we have reduced each robot to a point, we have to inflate each obstacle by the size of the robot radius to compensate.

## Slide 14: Configuration Space for a Mobile Robot

## Slide 15: Path Planning: Overview of Algorithms
3. Graph Search
  Identify a set edges between nodes within the free space
  Where to put the nodes?
1. Optimal Control
  Solves truly optimal solution
  Becomes intractable for even moderately complex as well as nonconvex problems
2. Potential Field
  Imposes a mathematical function over the state/configuration space
  Many physical metaphors exist
  Often employed due to its simplicity and similarity to optimal control solutions
Source:
http://mitocw.udsm.ac.tz
Configuration Space for a Mobile Robot

## Slide 16: Potential Field Path Planning Strategies
Robot is treated as a point under the influence of an artificial potential field.
Operates in the continuum
  Generated robot movement is similar to a ball rolling down the hill
  Goal generates attractive force
  Obstacle are repulsive forces
Khatib, 1986

## Slide 17: Potential Fields
Goal: Attractive Force
Large Distance --> Large Force
Model as Spring
Hooke's Law
F = -k X
Obstacles: Repulsive Force
Small Distance --> Large Force
Model as Electrically Charged Particles
Coulomb's law
F= k q1q2 / r2
Oussama Khatib, 1986.
Model navigation as the sum of forces on the robot

## Slide 18
attractive

## Slide 19
repulsive

## Slide 21: Potential Field Generation
Generation of potential field function U(q)
Generate artificial force field F(q)
Set robot speed (vx, vy) proportional to the force F(q) generated by the field
  the force field drives the robot to the goal

## Slide 22: Attractive Potential Field
q = [x, y]T qgoal = [xgoal, ygoal]T
Parabolic function representing the Euclidean distance
to the goal
Attracting force converges linearly towards 0 (goal)

## Slide 23: Repulsing Potential Field
Should generate a barrier around all the obstacle
  strong if close to the obstacle
  not influence if far from the obstacle
  minimum distance to the object, ρ0 distance of influence of object
  Field is positive or zero and tends to infinity as q gets closer to the object
obst.

## Slide 24: Repulsive potential field

## Slide 25: Potential Field Path Planning:
Notes:
  Local minima problem exists
  problem is getting more complex if the robot is not considered as a point mass
  If objects are non-convex there exists situations where several minimal distances exist ® can result in oscillations

## Slide 26: Computing the distance
In practice the distances are computed using sensors, such as range sensors which return the closets distance to obstacles

## Slide 27: Graph Algorithms
Methods
  Breath First
  Depth First
  Dijkstra
  A* and variants
  D* and variants
  ...

## Slide 28: Graph Construction: Cell Decomposition (1/4)
Divide space into simple, connected regions called cells
Determine which open cells are adjacent and construct a connectivity graph
Find cells in which the initial and goal configuration (state) lie and search for a path in the connectivity graph to join them.
From the sequence of cells found with an appropriate search algorithm, compute a path within each cell.
  e.g. passing through the midpoints of cell boundaries or by sequence of wall following movements.
Possible cell decompositions:
  Exact cell decomposition
  Approximate cell decomposition:
    Fixed cell decomposition
    Adaptive cell decomposition

## Slide 29: Graph Construction: Exact Cell Decomposition (2/4)

## Slide 30
Graph Construction: Approximate Cell Decomposition (3/4)

## Slide 31: Graph Construction: Adaptive Cell Decomposition (4/4)

## Slide 32: Graph Search Strategies: Breadth-First Search

## Slide 33: Dijkstra’s Algorithm
A generic path planning problem from vertex I to vertex
VI. The shortest path is I-II-III-V-VI with length 13.
Often highly inefficient
Notes: Starting from the initial vertex where
the path should start, the algorithm marks all direct neighbors
of the initial vertex with the cost to get there. It then proceeds
from the vertex with the lowest cost to all of its adjacent vertices
and marks them with the cost to get to them via itself
if this cost is lower. Once all neighbors of a vertex have been
checked, the algorithm proceeds to the vertex with the next
lowest cost. Once the algorithm reaches the goal vertex, it terminates
and the robot can follow the edges pointing towards
the lowest edge cost.

## Slide 34: Dijkstra’s Algorithm on a Grid

## Slide 35: Graph Search Strategies: A* Search
Similar to Dijkstra‘s algorithm, except that it uses a heuristic function h(n)
f(n) = g(n) + ε h(n)

## Slide 36: Dijkstra plus directional heuristic: A*

## Slide 37: Graph Search Strategies: D* Search
Similar to A* search, except that th search starts from the goal outward
f(n) = g(n) + ε h(n)
First pass is identical to A*
Subsequent passes reuse information from previous searches
For example when after executing the algorithm for a few times, new obstacles appear.

## Slide 38: Sampling-based Path Planning (or Randomized graph search)
When the state space is large complete solutions are often infeasible.
In practice, most algorithms are only resolution complete, i.e., only complete if the resolution is ne-grained enough
Sampling-based planners create possible paths by randomly adding points to a tree until some solution is found

## Slide 39: Rapidly Exploring Random Tree (RRT)
  Well suited for high-dimensional search spaces
  Often produces highly suboptimal solutions

## Slide 40: Probabilistic Roadmaps (PRM)
create a tree by randomly sampling points in the state-space
test whether they are collision-free
connect them with neighboring points using paths that reflects the kinematics of a robot
use classical graph shortest path algorithms to find shortest paths on the resulting structure.

## Slide 41: Planning at different length-scales

## Slide 42
Take-home lessons
First step in addressing a planning problem is choosing a suitable map representation
Reduce robot to a point-mass by inﬂating obstacles
Grid-based algorithms are complete, sampling-based ones probabilistically complete, but usually faster
Most real planning problems require combination of multiple algorithms

## Slide 43: Obstacle Avoidance (Local Path Planning)
The goal of the obstacle avoidance algorithms is to avoid collisions with obstacles
It is usually based on a local map
Often implemented as a more or less independent task
However, efficient obstacle avoidance should be optimal with respect to
  the overall goal
  the actual speed and kinematics of the robot
  the on boards sensors
  the actual and future risk of collision
Example: Alice
known obstacles (map)
Planed path
observed
obstacle
v(t), w(t)
Notes: goal: avoid obstacles
NOT path following
Creates local commands, usually with goal bias

## Slide 44: Obstacle Avoidance: Bug1
Following along the obstacle to avoid it
Each encountered obstacle is once fully circled before it is left at the point closest to the goal
Advantages
  No global map required
  Completeness guaranteed
Disadvantages
  Solutions are often
  highly suboptimal

## Slide 45: Obstacle Avoidance: Bug2
Following the obstacle always on the left or right side
Leaving the obstacle if the direct connection between start and goal is crossed